## Slide 1: Tutorial 3 Separation Process II (CHE F313)

## Slide 2: Problem 1
A crushed solid is subjected to a sieve analysis using a series of standard sieves. The following data are obtained:
Sieve aperture (mm) | Mass retained (g)
4.00 | 20
3.00 | 45
2.00 | 80
1.50 | 110
1.00 | 140
0.75 | 105
0.50 | 70
Pan | 30
Total | 600
Determine:
1. The differential screen analysis, i.e. the mass fraction and percentage of particles retained in each size range.
2. The cumulative analysis, including:
  a. cumulative percentage retained
  b. cumulative percentage passing
3. Plot the differential and cumulative size-distribution curves.
4. Estimate the 50% passing particle size (D₅₀) using interpolation.
  5. Calculate number of particles in each size fraction
6 Calculate the specific surface area of the particles assuming:
  a. particle density = 2500 kg/m³
  b. particles are approximately spherical
  c. shape factor = 1

## Slide 3: Problem 2
An irregular particle has a volume of 2.0× and a surface area of 5.5× . Its characteristic diameter is 1.5 mm.
Calculate the shape factor and the sphericity.